## Slide 1: Camera model and calibration
Samuel Cheng
Slide credit: James Tompkin, Naoh Snavely

## Slide 2: What is a camera?

## Slide 4: Camera obscura: dark room
Known during classical period in China and Greece (e.g., Mo-Ti, China, 470BC to 390BC)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys
James Hays

## Slide 5: Camera obscura / lucida used for tracing
Lens Based Camera Obscura, 1568
drawingchamber.wordpress.com
Camera lucida
Notes: https://drawingchamber.wordpress.com/about-me/about/camera-obscura-claude-glass-and-camera-lucida/
Obscura = dark
Lucida = light

## Slide 6: First Photograph
Oldest surviving photograph
  Took 8 hours on pewter plate
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 7: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 8
Notes: Paris town hall
“Anamorphosis” - a distorted projection or perspective requiring the viewer to use special devices or occupy a specific vantage point (or both) to reconstitute the image.

## Slide 10: Holbein’s The Ambassadors - 1533

## Slide 11: Holbein’s The Ambassadors – Memento Mori

## Slide 12: Pinhole camera model
Figure from Forsyth
d
d = Focal length (or f)
c = Optical center of the camera
c
Real object

## Slide 13: Modeling projection
Both (x’,y’,-d) and (x,y,z) project to the same point at PP
(x,y,z) -> (x’,y’) where x’ = d (x/z) and y’ = d (y/z)
PP: projection plane
COP: center of projection

## Slide 14: Modeling projection
Is the projection a linear transformation?
Homogeneous coordinates to the rescue!
Recall that:
homogeneous image
coordinates
homogeneous scene
coordinates
  no—division by z is nonlinear

## Slide 15: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
  The matrix is the projection matrix

## Slide 16: Perspective Projection
Note that scaling the projection matrix does not change the transform

## Slide 17: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 18: Variants of orthographic projection
Scaled orthographic
  Also called “weak perspective”
Affine projection
  Also called “paraperspective”

## Slide 19: Orthographic projection

## Slide 20: Perspective projection

## Slide 21: Perspective projection
What is preserved?
Straight lines are still straight.

## Slide 22: Vanishing points and lines
Parallel lines in the world
intersect in the projected image at a “vanishing point”.
Parallel lines on the same plane in the world converge to vanishing points on a “vanishing line”.
E.G., the horizon.
Vanishing Point
Vanishing Point
Vanishing Line
Notes: Various properties of vanishing points/lines.
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 23: Vanishing points and lines
Vanishing
point
Vanishing
point
Vertical vanishing
point
(at infinity)
Slide from Efros, Photo from Criminisi

## Slide 24: Projection properties
Many-to-one: any points along same ray map to same point in image
Points → points
Lines → lines
But line through focal point projects to a point
Planes → planes (or half-planes)
  But plane through focal point projects to line

## Slide 25: Camera parameters
How many numbers do we need to describe a camera?
We need to describe its pose in the world
We need to describe its internal parameters

## Slide 26: A Tale of Two Coordinate Systems
“The World”
Camera
x
y
z
v
w
u
o
COP
Two important coordinate systems:
1. World coordinate system
2. Camera coordinate system

## Slide 27: Camera parameters
To project a point (x,y,z) in world coordinates into a camera
First transform (x,y,z) into camera coordinates
Need to know extrinsics
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)
Then project into the image plane
  Need to know camera intrinsics
  Coming soon
These can all be described with matrices

## Slide 28: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c

## Slide 29: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?

## Slide 30: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix

## Slide 31: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R

## Slide 32: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
projection
intrinsics
rotation
translation
identity matrix
A camera is described by several parameters
  Translation T of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f, principle point (x’c, y’c), pixel size (sx, sy)
  blue parameters are called “extrinsics,” red are “intrinsics”
  The definitions of these parameters are not completely standardized
    especially intrinsics—varies from one book to another

## Slide 33
Slide Credit: Savarese
Camera (projection) matrix
x: Image Coordinates: (U,V,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,t
X
x
Extrinsic Matrix
Notes: We can use homogeneous coordinates to write ‘camera matrix’ in linear form.

## Slide 34
K
Slide Credit: Savarese
Projection matrix (ignore extrinsics)
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
(0,0,0)
di
O’
Notes: Work through equations for u and v on board

## Slide 35
K
Slide Credit: Savarese
Remove assumption: aligned optical center
Intrinsic Assumptions
Unit aspect ratio
Optical center at -(U0,V0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
(0,0,0)
di
O’
O’
Notes: Work through equations for u and v on board

## Slide 36: Perspective distortion
Problem for architectural photography: converging verticals
Source: F. Durand

## Slide 37: Perspective distortion
Problem for architectural photography: converging verticals
Solution: view camera (lens shifted w.r.t. film)
Source: F. Durand
Tilting the camera upwards results in converging verticals
Keeping the camera level, with an ordinary lens, captures only the bottom portion of the building
Shifting the lens upwards results in a picture of the entire subject
http://en.wikipedia.org/wiki/Perspective_correction_lens

## Slide 38: Perspective distortion
Problem for architectural photography: converging verticals
Result:
Source: F. Durand

## Slide 39
K
Slide Credit: Savarese
Remove assumption: aligned optical center
Intrinsic Assumptions
Unit aspect ratio
Optical center at -(U0,V0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
(0,0,0)
di
O’
O’
Notes: Work through equations for u and v on board

## Slide 40
K
Slide Credit: Savarese
Remove assumption: unit aspect ratio
Intrinsic Assumptions
Optical center at -(U0,V0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
(0,0,0)
di
O’
O’
Notes: Work through equations for u and v on board

## Slide 41
K
Slide Credit: Savarese
Remove assumption: non-skewed pixels
Intrinsic Assumptions
Optical center at -(U0,V0)
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
(0,0,0)
di
O’
O’
Notes: Work through equations for u and v on board

## Slide 42: Summary
James Hays

## Slide 43: Camera Matrix DEMO

## Slide 44: Beyond Pinholes: Radial Distortion
Image from Martin Habbecke
Corrected Barrel Distortion
Radial distortion can be introduced due to the use of lens
.
.
.

## Slide 45: Radial distortion
Radial distortion can be reduced by the following correction
r is the radial distance from the center of the scene
The parameters can be estimated by shooting straight lines since a straight line is supposed to be preserved under perspective projection

## Slide 46: World vs Camera coordinates
James Hays

## Slide 47: Calibrating the Camera
Use an scene with known geometry
  Correspond image points to 3d points
  Get least squares solution (or non-linear solution)
Known 3d
world locations
Known 2d image coords
Unknown Camera Parameters
James Hays
M

## Slide 48: How do we calibrate a camera?
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
308.253 306.300 28.881
306.650 309.301 28.905
308.069 306.831 29.189
309.671 308.834 29.029
308.255 309.955 29.267
307.546 308.613 28.963
311.036 309.206 28.913
307.518 308.175 29.069
309.950 311.262 29.990
312.160 310.772 29.080
311.988 312.709 30.514
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
317 335
783 521
235 427
665 429
655 362
427 333
412 415
746 351
434 415
525 234
716 308
602 187
Known 3d world locations
Known 2d image coords
James Hays

## Slide 49
Known 3d locations
Known 2d image coords
Unknown Camera Parameters
James Hays
Two equations per 3D point correspondence
First, work out where X,Y,Z projects to under candidate M.

## Slide 50
Known 3d locations
Known 2d image coords
Unknown Camera Parameters
Next, rearrange into form where all M coefficients are individually stated in terms of X,Y,Z,u,v.
-> Allows us to form lsq matrix.

## Slide 51
Known 3d locations
Known 2d image coords
Unknown Camera Parameters
Next, rearrange into form where all M coefficients are individually stated in terms of X,Y,Z,u,v.
-> Allows us to form lsq matrix.

## Slide 52
Finally, solve for m’s entries using linear least squares
Method 1 –
Ax=b form
M = A\Y;
M = [M;1];
M = reshape(M,[],3)';
Known 3d locations
Known 2d image coords
James Hays
Unknown Camera Parameters
Notes: Method 1 – nonhomogeneous linear system. Not related to homogeneous coordinates!! - https://en.m.wikipedia.org/wiki/System_of_linear_equations

## Slide 53
Known 3d locations
Known 2d image coords
Or, solve for m’s entries using total linear least-squares.
Method 2 –
[U, S, V] = svd(A);
M = V(:,end);
M = reshape(M,[],3)';
Ax=0 form
James Hays
Unknown Camera Parameters
Notes: Method 2 – homogeneous linear system. Not related to homogeneous coordinates!! - https://en.m.wikipedia.org/wiki/System_of_linear_equations

## Slide 54: How do we calibrate a camera?
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
308.253 306.300 28.881
306.650 309.301 28.905
308.069 306.831 29.189
309.671 308.834 29.029
308.255 309.955 29.267
307.546 308.613 28.963
311.036 309.206 28.913
307.518 308.175 29.069
309.950 311.262 29.990
312.160 310.772 29.080
311.988 312.709 30.514
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
317 335
783 521
235 427
665 429
655 362
427 333
412 415
746 351
434 415
525 234
716 308
602 187
Known 3d world locations
Known 2d image coords
James Hays

## Slide 55
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
…..
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
335
…
Known 3d world locations
Known 2d image coords
1st point
Projection error defined by two equations – one for u and one for v

## Slide 56
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
…..
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
335
…
Known 3d world locations
Known 2d image coords
2nd point
Projection error defined by two equations – one for u and one for v

## Slide 57: How many points do I need to fit the model?
5
6
Degrees of freedom?
Think 3:
Rotation around x
Rotation around y
Rotation around z
Notes: How many known points are needed to estimate this?
Why 5?
Why 6? Don’t we have 12 parameters here?
But matrix is not full rank -> it’s a projection (we can tell because it isn’t square -> the column space is 4D, but the row space is 3D, so this matrix projects a 4D space to a 3D space)
One of the dimensions is lost – intuitive, dimensionality reduction machine.
Ambiguous scale in the camera projection matrix. This scale is in the null space of the matrix, i.e., there is a line of possible solutions (plane?)

## Slide 58: How many points do I need to fit the model?
5
6
Degrees of freedom?
M is 3x4, so 12 unknowns, but projective scale ambiguity – 11 deg. freedom.
One equation per unknown -> 5 1/2 point correspondences determines a solution (e.g., either u or v).
More than 5 1/2 point correspondences -> overdetermined, many solutions to M.
Least squares is finding the solution that best satisfies the overdetermined system.
Why use more than 6? Robustness to error in feature points.
Notes: How many known points are needed to estimate this?
Why 5?
Why 6? Don’t we have 12 parameters here?
8 equations in 2D -> 16 parameters
But matrix is not full rank -> it’s a projection (we can tell because it isn’t square -> the column space is 4D, but the row space is 3D, so this matrix projects a 4D space to a 3D space)
One of the dimensions is lost – intuitive, dimensionality reduction machine.
Ambiguous scale in the camera projection matrix. This scale is in the null space of the matrix, i.e., there is a line of possible solutions (plane?)
Actually only need 8 points to produce a valid (up to scale) projection matrix.

## Slide 59: Solving - why two methods?
Any projection is inherently ambiguous
A space of possible solutions
Under projective model, this is our projective scale ambiguity.
x1
x
v1
v2

## Slide 60: Calibration with linear method
Advantages
  Easy to formulate and solve
  Provides initialization for non-linear methods
Disadvantages
  Doesn’t directly give you camera parameters
  Doesn’t model radial distortion
  Can’t impose constraints, such as known focal length
Non-linear methods are preferred
  Define error as difference between projected points and measured points
  Minimize error using Newton’s method or other non-linear optimization
James Hays

## Slide 61: Can we factorize M back to K [R | T]?
Yes!
We can directly solve for the individual entries of K [R | T].
James Hays

## Slide 62
James Hays
an = nth column of A

## Slide 63
James Hays

## Slide 64
James Hays

## Slide 65: Can we factorize M back to K [R | T]?
Yes!
We can also use RQ factorization (not QR)
  R in RQ is not rotation matrix R; crossed names!
R (right diagonal) is K
Q (orthogonal basis) is R.
T, the last column of [R | T], is inv(K) * last column of M.
  But you need to do a bit of post-processing to make sure that the matrices are valid. See http://ksimek.github.io/2012/08/14/decompose/
James Hays

## Slide 66: Recovering the camera center
Q
James Hays
m4
t
C=-R-1 K-1 m4

## Slide 67: Recovering the camera center
This is not the camera center C.
It is –RC, as the point is rotated before tx, ty, and tz are added
This is t × K
Q
So K-1 m4 is t
So we need -R-1 K-1 m4 to get C.
Q is K × R.
So we just need -Q-1 m4
James Hays
m4
t

## Slide 68: Estimate of camera center
1.5706 -0.1490 0.2598
-1.5282 0.9695 0.3802
-0.6821 1.2856 0.4078
0.4124 -1.0201 -0.0915
1.2095 0.2812 -0.1280
0.8819 -0.8481 0.5255
-0.9442 -1.1583 -0.3759
0.0415 1.3445 0.3240
-0.7975 0.3017 -0.0826
-0.4329 -1.4151 -0.2774
-1.1475 -0.0772 -0.2667
-0.5149 -1.1784 -0.1401
0.1993 -0.2854 -0.2114
-0.4320 0.2143 -0.1053
-0.7481 -0.3840 -0.2408
0.8078 -0.1196 -0.2631
-0.7605 -0.5792 -0.1936
0.3237 0.7970 0.2170
1.3089 0.5786 -0.1887
1.2323 1.4421 0.4506
1.0486 -0.3645
-1.6851 -0.4004
-0.9437 -0.4200
1.0682 0.0699
0.6077 -0.0771
1.2543 -0.6454
-0.2709 0.8635
-0.4571 -0.3645
-0.7902 0.0307
0.7318 0.6382
-1.0580 0.3312
0.3464 0.3377
0.3137 0.1189
-0.4310 0.0242
-0.4799 0.2920
0.6109 0.0830
-0.4081 0.2920
-0.1109 -0.2992
0.5129 -0.0575
0.1406 -0.4527

## Slide 69: Calibration example