## Slide 1: Pixels and Filters
Samuel Cheng
Slide credits: Juan Carlos Niebles, Ranjay Krishna, James Hays, Noah Snavely

## Slide 2: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 3: Types of Images

## Slide 4: Types of Images

## Slide 5: Types of Images

## Slide 6: Binary image representation
Slide credit: Ulas Bagci

## Slide 7: Grayscale image representation
Slide credit: Ulas Bagci

## Slide 8: Color Image - one channel
Slide credit: Ulas Bagci

## Slide 9: Color image representation
Slide credit: Ulas Bagci

## Slide 10: Images are sampled
What happens when we zoom into the images we capture?

## Slide 11: Errors due Sampling
Slide credit: Ulas Bagci

## Slide 12: Resolution
is a sampling parameter, defined in dots per inch (DPI) or equivalent measures of spatial pixel density, and its standard value for recent screen technologies is 72 dpi
Slide credit: Ulas Bagci

## Slide 13: Images are Sampled and Quantized
An image contains discrete number of pixels
  A simple example
  Pixel value:
    “grayscale”
    (or “intensity”): [0,255]
231
75
148
Notes: Last time: Images as Matrices
intensity
temperature
depth

## Slide 14: Images are Sampled and Quantized
An image contains discrete number of pixels
  A simple example
  Pixel value:
    “grayscale”
    (or “intensity”): [0,255]
    “color”
      RGB: [R, G, B]
      Lab: [L, a, b]
      HSV: [H, S, V]
[249, 215, 203]
[90, 0, 53]
[213, 60, 67]

## Slide 15: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 16: Histogram
Histogram of an image provides the frequency of the brightness (intensity) value in the image.
def histogram(im):
h = np.zeros(255)
for row in im.shape[0]:
for col in im.shape[1]:
val = im[row, col]
h[val] += 1
function h=histogram(im)
h=zeros(1,255);
for row=1:size(im,1)
for col=1:size(im,2)
val = im(row,col)+1;
h(val)=h(val)+1;
end
end
end

## Slide 17: Histogram
Slide credit: Dr. Mubarak Shah

## Slide 18: A use case: histogram equalization

## Slide 19: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 20: Images as functions
Images are usually digital (discrete):
  Sample the 2D space on a regular grid
Represented as a matrix of integer values
pixel

## Slide 21: Images as functions
Cartesian coordinates
Notation for
discrete
functions

## Slide 22: Images as functions
An Image as a function f from R2 to RM:
  f( x, y ) gives the intensity at position ( x, y )
  Defined over a rectangle, with a finite range:
    f: [a,b] x [c,d ]  [0,255]
Domain
support
range

## Slide 23: Images as functions
An Image as a function f from R2 to RM:
  f( x, y ) gives the intensity at position ( x, y )
  Defined over a rectangle, with a finite range:
    f: [a,b] x [c,d ]  [0,255]
A color image:
Domain
support
range
Notes: Each r, g, b are functions that like the one above

## Slide 24: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 25: Systems and Filters
Filtering:
  Forming a new image whose pixel values are transformed from original pixel values
Goals:
Goal is to extract useful information from images, or transform images into another domain where we can modify/enhance image properties
  Features (edges, corners, blobs…)
  super-resolution; in-painting; de-noising

## Slide 26: System and Filters
we define a system as a unit that converts an input function f[n,m] into an output (or response) function g[n,m], where (n,m) are the independent variables.
  In the case for images, (n,m) represents the spatial position in the image.

## Slide 27
Super-resolution
De-noising
In-painting
Bertamio et al

## Slide 28: Images as functions
Cartesian coordinates
Notation for
discrete
functions

## Slide 29: 2D discrete-space systems (filters)
S is the system operator, defined as a mapping or assignment of a member of the set of possible outputs g[n,m] to each member of the set of possible inputs f[n,m].

## Slide 30: Filter example #1: Box filter
2D DS moving average over a 3 × 3 window of neighborhood
1
1
1
1
1
1
1
1
1
h
Notes: Board:
Input image
Output image
each pixel results from a neighborhood operation

## Slide 31
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 32
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 33
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 34
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 35
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 36
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 37
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 38
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 39
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 40
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
Why does it sum to one?
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 41
Smoothing with box filter
James Hays

## Slide 42: Image filtering
Image filtering:
  Compute function of local neighborhood at each position
Really important!
  Enhance images
    Denoise, resize, increase contrast, etc.
  Extract information from images
    Texture, edges, distinctive points, etc.
  Detect patterns
    Template matching
James Hays

## Slide 43: Think-Pair-Share time
0
0
0
0
1
0
0
0
0
1.
0
0
0
1
0
0
0
0
0
2.
-1
0
1
-2
0
2
-1
0
1
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
3.
4.

## Slide 44: 1. Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 45: 1. Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 46: 2. Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 47: 2. Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 48: 3. Practice with linear filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel
David Lowe

## Slide 49: 3. Practice with linear filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel
David Lowe
Notes: Questions at this point?

## Slide 50: 4. Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 51: 4. Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe

## Slide 52: 4. Practice with linear filters
Source: D. Lowe

## Slide 53: Filter example #2: Image Segmentation
Image segmentation based on a simple threshold:
255,

## Slide 54: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity
  Linearity
  (Linearity => additivity)
  Stability
  Invertibility

## Slide 55: Properties of systems
Spatial properties
  Causality
  Shift invariance:

## Slide 56: Is the moving average system is shift invariant?
Yes!

## Slide 57: Linear Systems (filters)
Is the moving average a linear system?
Is thresholding a linear system?
  f1[n,m] + f2[n,m] > T
  f1[n,m] < T
  f2[n,m]<T
No!
Yes!
Notes: Show on the board equations for moving average.

## Slide 58: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 59: Correlation
This is called a (cross-)correlation operation:
Let be the image, be the kernel (of size 2k+1 x 2k+1), and be the output image
Can think of as a “dot product” between local neighborhood and kernel for each pixel

## Slide 60: Convolution
Same as cross-correlation, except that the kernel is “flipped” (horizontally and vertically)
This is called a convolution operation:

## Slide 61: Commutative property
H*F=F*H if we can ignore the boundary condition (k >> i,j)

## Slide 62: Associative property

## Slide 63: Convolution properties
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
  Correlation is _not_ associative
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = [0, 0, 1, 0, 0], a * e = a
Source: S. Lazebnik
Notes: David Jacobs @ UMD http://www.cs.umd.edu/~djacobs/CMSC426/Convolution.pdf
The key difference between the two is that convolution is associative. That is, if F and G are filters, then F*(G*I) = (F*G)*I. If you don’t believe this, try a simple example, using F=G=(-1 0 1), for example. It is very convenient to have convolution be associative. Suppose, for example, we want to smooth an image and then take its derivative. We could do this by convolving the image with a Gaussian filter, and then convolving it with a derivative filter. But we could alternatively convolve the derivative filter with the Gaussian to produce a filter called a Difference of Gaussian (DOG), and then convolve this with our image. The nice thing about this is that the DOG filter can be precomputed, and we only have to convolve one filter with our image.
In general, people use convolution for image processing operations such as smoothing, and they use correlation to match a template to an image. Then, we don’t mind that correlation isn’t associative, because it doesn’t really make sense to combine two templates into one with correlation, whereas we might often want to combine two filter together for convolution. When discussing the Fourier series as a way of understanding filtering, we will use convolution, so that we can introduce the famous convolution theorem.

## Slide 64: Correlation and Convolution
2d correlation
2d convolution
  Imfilter(Imfilter(I,f),g)!= imfilter(I,imfilter(f,g))
conv2(I,f)is the same as filter2(rot90(f,2),I)
Correlation and convolution are identical when the filter is symmetric.
James Hays
  h=filter2(f,I); or h=imfilter(I,f);
  h=conv2(f,I); or h=imfilter(I,f,’conv’);

## Slide 65: Key properties of linear filters
Linearity:
imfilter(I, f1 + f2) =
imfilter(I,f1) + imfilter(I,f2)
Shift invariance: Same behavior regardless of pixel location
imfilter(I,shift(f)) = shift(imfilter(I,f))
Any linear, shift-invariant operator can be represented as a convolution
Source: S. Lazebnik
Notes: f is image

## Slide 66: LSI (linear shift invariant) systems
An LSI system is completely specified by its impulse response.
Discrete convolution
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 67: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 68: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 69: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 70: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 71: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 72: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 73: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 74: Image support and edge effect
A computer will only convolve finite support signals.
  That is: images that are zero for n,m outside some rectangular region
numpy’s convolution performs 2D convolution of finite-support signals.
N1 ×M1
N2 ×M2
(N1 + N2 − 1) × (M1 +M2 − 1)
*
=

## Slide 75: Image support and edge effect
A computer will only convolve finite support signals.
What happens at the edge?
f
h
• zero “padding”
• edge value replication
• mirror extension
• more (beyond the scope of this class)
-> Matlab conv2 uses zero-padding

## Slide 76
Slide credit: Wolfram Alpha

## Slide 77: properties
• Associative property:
• Distributive property:
The order doesn’t matter!

## Slide 78: properties
• Shift property:
• Shift-invariance:

## Slide 79: Convolution vs. (Cross) Correlation
A convolution is an integral that expresses the amount of overlap of one function as it is shifted over another function.
  convolution is a filtering operation
Correlation compares the similarity of two sets of data. Correlation computes a measure of similarity of two input signals as they are shifted by one another. The correlation result reaches a maximum at the time when the two signals match best .
  correlation is a measure of relatedness of two signals

## Slide 80: Convolution vs. (Cross) Correlation
 | Convolution | Correlation
Associative: (ab)c=a(bc) | Yes | No
Commutative: ab=ba | Yes | No
Distributive: a(b+c)=ab+ac | Yes | Yes
Linear | Yes | Yes
Application | Filtering | Matching
They are equivalent when the kernel is symmetric

## Slide 81: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 82
Weight contributions of neighboring pixels by nearness
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Slide credit: Christopher Rasmussen
Important filter: Gaussian
x
y
x
y
Notes: e^0 = 1, e^-1 = .37, e^-2 = .14, etc.

## Slide 83
Smoothing with Gaussian filter
James Hays

## Slide 84
Smoothing with box filter
James Hays

## Slide 85: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
  Images become more smooth
Gaussian convolved with Gaussian… …is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width σ√2
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 86: Separability of the Gaussian filter
Source: D. Lowe

## Slide 87: Separability example
*
*
=
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:
=
Notes: Convolution vs filtering doesn’t matter here because the filter is symmetric
9 multiply-add operations at the top for 2D convolution
~11 multiply-add operations at the bottom for the separable 2D convolution

## Slide 88: Separability
Why is separability useful in practice?

## Slide 89: Separability
Why is separability useful in practice?
MxN image, PxQ filter
2D convolution: ~MNPQ multiply-adds
Separable 2D: ~MN(P+Q) multiply-adds
Speed up = PQ/(P+Q)
9x9 filter = ~4.5x faster
Notes: https://blogs.mathworks.com/steve/2006/10/04/separable-convolution/

## Slide 90: Practical matters
How big should the filter be?
Values at edges should be near zero
Gaussians have infinite extent…
Rule of thumb for Gaussian: set filter half-width to about 3 σ
James Hays

## Slide 91: Filtering in frequency domain
Can be faster than filtering in spatial domain (for large filters)
Can help understand effect of filter
Algorithm:
  Convert image and filter to fft (fft2 in matlab)
  Pointwise-multiply ffts
  Convert result to spatial domain with ifft2
Hays

## Slide 92: Examples
Edge filter (high-pass)
Gaussian filter (low-pass)
FFT of Gaussian
[-1 1]
FFT of Gradient Filter
Gaussian
Hays

## Slide 93: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 94: Median filters
Operates over a window by selecting the median intensity in the window.
‘Rank’ filter as based on ordering of gray levels
  E.G., min, max, range filters
Steve Seitz, Steve Marschner
Notes: Better at salt’n’pepper noise
Not convolution: try a region with 1’s and a 2, and then 1’s and a 3

## Slide 95
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering - mean
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 96
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering - mean
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 97
 |  |  |  | ? |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Median filter?
Credit: S. Seitz
Notes: Answer is 90.

## Slide 98: Median filters
Operates over a window by selecting the median intensity in the window.
What advantage does a median filter have over a mean filter?
Steve Seitz, Steve Marschner
Notes: Better at salt’n’pepper noise

## Slide 99: Noisy Jack – Salt and Pepper
Notes: No, not the latest smash hit from early 90’s hip hop group

## Slide 100: Mean Jack – 3 x 3 filter

## Slide 101: Very Mean Jack – 11 x 11 filter

## Slide 102: Noisy Jack – Salt and Pepper
Notes: No, not the latest smash hit from early 90’s hip hop group

## Slide 103: Median Jack – 3 x 3

## Slide 104: Very Median Jack – 11 x 11

## Slide 105: Median filters
Operates over a window by selecting the median intensity in the window.
What advantage does a median filter have over a mean filter?
Is a median filter a kind of convolution?
Secret: Median filtering is sorting.
Is median filter linear?
Steve Seitz, Steve Marschner
Notes: Answer: Not convolution: try a region with 1’s and a 2, and then 1’s and a 3

## Slide 106: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter