## Slide 1: ECE 4973: Lecture 3 Image Filters
Samuel Cheng
Slide credits: Juan Carlos Niebles, Ranjay Krishna, James Hays, Noah Snavely

## Slide 2: Image resolution vs radiometric Resolution
8 bit – 256 levels
1 bit – 2 levels
2 bit – 4 levels
4 bit – 16 levels

## Slide 3: What we have learned today?
Image histograms
Linear systems (filters)
Convolution and correlation
Gaussian filter
Median filter

## Slide 4: Systems and Filters
Filtering:
  Forming a new image whose pixel values are transformed from original pixel values
Goals:
Enhance image: super-resolution; in-painting; de-noising
Extract useful information: features (edge, corners, blobs, etc.) extraction
Preprocessing: transform images into another domain for easier processing (Fourier transform)

## Slide 5: System and Filters
Notes: we define a system as a unit that converts an input signal f[n,m] into an output (or response) signal g[n,m], where (n,m) are the independent variables.
  In the case for images, (n,m) represents the spatial position in the image.

## Slide 6
Super-resolution
De-noising
In-painting
Bertamio et al

## Slide 7: Grayscale images as 2D signals
Cartesian coordinates
Notation for
discrete
signal

## Slide 8: Filter example #1: Box filter
2D DS moving average over a 3 × 3 window of the target pixel’s neighborhood
1
1
1
1
1
1
1
1
1
Notes: Board:
Input image
Output image
each pixel results from a neighborhood operation

## Slide 9: Image filtering
Image filtering:
  Compute function of local neighborhood at each position
Really important!
  Enhance images
    Denoise, resize, increase contrast, etc.
  Extract information from images
    Texture, edges, distinctive points, etc.
  Detect patterns
    Template matching
James Hays

## Slide 10
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 11
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 12
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 13
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 14
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 15
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 16
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
 |  |  |  | 50 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
?
Notes: ones, divide by 9

## Slide 17
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz

## Slide 18
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 19
What does it do?
Replaces each pixel with an average of its neighborhood
Achieve smoothing effect (remove sharp features)
Why does it sum to one?
1
1
1
1
1
1
1
1
1
Slide credit: David Lowe (UBC)
Box Filter

## Slide 20
Smoothing with box filter
James Hays

## Slide 21: Linear filter
Homogeneous?
Additive?
Stable?
Invertible?

## Slide 22: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity
  Linearity
  (Linearity => additivity)
  Stability
  Invertibility

## Slide 23: Think-Pair-Share time
0
0
0
0
1
0
0
0
0
1.
0
0
0
1
0
0
0
0
0
2.
-1
0
1
-2
0
2
-1
0
1
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
3.
4.

## Slide 24: 1. Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 25: 1. Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 26: 2. Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 27: 2. Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 28: 3. Practice with linear filters
-1
0
1
-2
0
2
-1
0
1
Vertical Edge
(absolute value)
Sobel
David Lowe
1
2
1
1 | 0 | -1
*
=

## Slide 29: 3. Practice with linear filters
-1
-2
-1
0
0
0
1
2
1
Horizontal Edge
(absolute value)
Sobel
David Lowe
Notes: Questions at this point?

## Slide 30: 4. Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 31: 4. Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe
Aka unsharp masking

## Slide 32: 4. Practice with linear filters
Source: D. Lowe

## Slide 33: Shift-invariance and linearity

## Slide 34: Two important properties of systems
Shift invariance (same behavior regardless of pixel location)
Linearity
Equivalently: S(I,shift(f)) = shift(S(I,f))
Notes: LHS: g[n-no]
RHS: S[f[n-n0]]

## Slide 35: Is the moving average system is shift invariant?
Yes!

## Slide 36: Linear Systems (filters)
Is the moving average a linear system?
Yes!
Notes: Show on the board equations for moving average.

## Slide 37: Filter example #2: Image Segmentation
Image segmentation based on a simple threshold:
255,

## Slide 38: Simple thresholding
Is thresholding shift-invariant?
Is thresholding a linear system?
  f1[n,m] + f2[n,m] > T
  f1[n,m] < T
  f2[n,m]<T
No!
Yes!
Notes: Show on the board equations for moving average.

## Slide 39: Convolution and correlation

## Slide 40: Correlation (we are doing so far)
This is called a (cross-)correlation operation:
Let be the image, be the kernel (filter), and be the output image
Can think of as a “dot product” between local neighborhood and kernel for each pixel

## Slide 41: Convolution
Same as cross-correlation, except that the kernel is “flipped” (horizontally and vertically)
This is called a convolution operation:

## Slide 42: Where is convolution coming from?
1-D: ]

## Slide 43: Why do mathematicians and signal processing researchers like convolution?
Any linear and shift-invariant operator can be represented as a convolution (and specified by its impulse response)
Source: S. Lazebnik
Notes: f is image

## Slide 44: Commutative property
H*F=F*H if we can ignore the boundary condition (k >> i,j)

## Slide 45: Associative property

## Slide 46: What is ? A result we need in the next slide …

## Slide 47: Convolution properties
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
  Correlation is NOT associative
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = [0, 0, 1, 0, 0], a * e = a
Source: S. Lazebnik
Notes: David Jacobs @ UMD http://www.cs.umd.edu/~djacobs/CMSC426/Convolution.pdf
The key difference between the two is that convolution is associative. That is, if F and G are filters, then F*(G*I) = (F*G)*I. If you don’t believe this, try a simple example, using F=G=(-1 0 1), for example. It is very convenient to have convolution be associative. Suppose, for example, we want to smooth an image and then take its derivative. We could do this by convolving the image with a Gaussian filter, and then convolving it with a derivative filter. But we could alternatively convolve the derivative filter with the Gaussian to produce a filter called a Difference of Gaussian (DOG), and then convolve this with our image. The nice thing about this is that the DOG filter can be precomputed, and we only have to convolve one filter with our image.
In general, people use convolution for image processing operations such as smoothing, and they use correlation to match a template to an image. Then, we don’t mind that correlation isn’t associative, because it doesn’t really make sense to combine two templates into one with correlation, whereas we might often want to combine two filter together for convolution. When discussing the Fourier series as a way of understanding filtering, we will use convolution, so that we can introduce the famous convolution theorem.

## Slide 48: Correlation and Convolution
2d correlation
2d convolution
  Imfilter(Imfilter(I,f),g)!= imfilter(I,imfilter(f,g))
conv2(I,f)is the same as filter2(rot90(f,2),I)
≡ filter2(fliplr(flipud((f,2)),I)
Correlation and convolution are identical when the filter is symmetric.
James Hays
  h=filter2(f,I); or h=imfilter(I,f);
  h=conv2(f,I); or h=imfilter(I,f,’conv’);

## Slide 49: Image support and edge effect
A computer will only convolve finite support signals.
  That is: images that are zero for n,m outside some rectangular region
numpy’s convolution performs 2D convolution of finite-support signals.
N1 ×M1
N2 ×M2
(N1 + N2 − 1) × (M1 +M2 − 1)
*
=

## Slide 50: Image support and edge effect
A computer will only convolve finite support signals.
What happens at the edge?
f
h
• zero “padding”
• edge value replication
• mirror extension
• more (beyond the scope of this class)
-> Matlab conv2 uses zero-padding

## Slide 51
Slide credit: Wolfram Alpha

## Slide 52: properties
• Associative property:
• Distributive property:
The order doesn’t matter!

## Slide 53: properties
• Shift property:
• Shift-invariance:

## Slide 54: Convolution vs. (Cross) Correlation
A convolution is a filtering operation
Correlation compares the similarity of two sets of data
Notes: . The correlation result reaches a maximum at the time when the two signals match best .
  correlation is a measure of relatedness of two signals

## Slide 55: Convolution vs. (Cross) Correlation
 | Convolution | Correlation
Associative: (ab)c=a(bc) | Yes | No
Commutative: ab=ba | Yes | No
Distributive: a(b+c)=ab+ac | Yes | Yes
Linear | Yes | Yes
Application | Filtering | Matching
They are equivalent when the filter “kernel” is symmetric
N.B. cv2.filter2D implements correlation rather than conv
Notes: In CV, most filters (not all) we considered are symmetric. So they are the same.